Above is a drawing of a table top planter which can accommodate seated and wheelchair gardening.

Dimensions

For a table top bed to allow the gardener to sit face on to the soil surface, whilst legs and chair fit under, table top heights range between 63 - 75cm from the ground depending on the height of the chair to be accommodated and to allow for easy reaching over sides of the bed.

Depending on the strength of the table bed construction and the clearance required for chair and person, the soil bed can vary from 25cm - 35cm.

Materials and finishes

- Use Pressure treated wood, suitable for external use

- Thick plywood (suitable for external use) for base of planter, drilled with drainage holes

- Use non-rusting screws and fixings (non-ferrous) suitable for outdoors

- waterproofing finish /lining on inside surfaces of bed

Drawing kindly provided by Annie Pollock, Arterre Landscapes, 20 Leamington Terrace

Edinburgh EH10 4JN

© Trellis. All rights reserved.

The information contained in this briefing was correct at publication.

This information is provided by Trellis and while we endeavour to ensure information is up to date and correct, we make no representations or warranties of any kind, express or implied, about the completeness, accuracy, reliability, suitability or availability with respect to the briefing or the information, products, services, or related graphics contained on the websites for any purpose. Any reliance you place on such information is therefore strictly at your own risk. If you would like to contribute material to this resource, please email info@trellisscotland.org.uk